### Wildfire Risk and Hazard Assessment Checklist

#### Zone 1 – Primary Protection Area

###### Firefighter egress –

###### Access and escape routes and maneuvering room are adequate for safe movement

###### Access and escape routes and maneuvering room are inadequate for safe movement 	(roadways and turnarounds suitable for fire fighting equipment should be provided)

##### Roofing Materials

- Roofing material is “C class” or better on all structures

- Some roofing material is less than “C class”… (appropriate roofing should be installed)

###### Vegetation

- Type

- Light (e.g., grasses, sawgrass, and tundra)

- Medium (e.g., light brush and small trees)

- Heavy (e.g., timber, hardwoods, heavy brush)… vegetation should be pruned, thinned, or removed to reduce the hazard

- Slash (e.g., timber harvesting residue)… vegetation should be pruned, thinned, or removed to reduce the hazard

- Clearing

- 15 feet of cleared space is maintained around all structures

- Less than 15 feet of cleared space is maintained around 1 or more of the structures… (vegetation should be removed or reduced in this area)

##### Flammables / Combustibles

- LP tank (if present) is > 25’ from the structure and the end of the tank is not pointed at it

- There are no gasoline cans, LP grill bottles, or other flammables in unidentified storage sheds or laying around on the property

- LP tank is within 25’ of the structure and/or the end of the tank is pointing at it… (rectify the location and/or alignment of the LP tank)

- Gasoline cans, LP grill bottles, or other flammables are present in unidentified storage sheds or laying around on the property… (these should be consolidated, properly stored, and identified)

##### Chimneys and flues

- Spark arrestors or woven wire mesh have installed over all chimneys/flues

- Vegetation has been removed from within 10 feet of all flues/chimneys

- Vegetation has not been removed from within 10 feet of flues/chimneys (chimneys/flues should be modified to include a spark arrestor)

##### Utilities (all new construction should have underground utilities)

- Utilities are underground

- Utilities can easily be relocated underground (should be buried as soon as possible)

- Utilities are above ground (vegetation clearing critical; reduce damage potential)

# Zone 2 – Fuel Reduction Area

- Area between 75 and 125 feet has had vegetation reduced

- Area between 75 and 125 feet is overgrown (area should have material reduced)

##### Zone 3 – Balance of Property

- Vegetation is healthy and free of insect infestation

- Area has adequate fire access for fire-fighters

- Dead, diseased, insect infested, or otherwise unhealthy shrubs, trees, and limbs are present (such material should be pruned or removed)

- Fire fighter access is inadequate to unimproved areas (fire trails or roads should be constructed)

If the property owner will not take the steps to reduce the risk, the fire service may red-tag the property so as to not endanger the life and limb of the fire fighters.